## Slide 1: Lab 5 IoT Wired Communication Protocols
2021.05.06

## Slide 2: Wired Communication for IoT
Internal wired communication
  I2C
  SPI
External wired communication
  Ethernet
  RS-232
  RS-485
  UART/USART
  USB
Notes: https://www.strongpilab.com/rs232-uart-difference/

## Slide 3: Half-Duplex/Full-Duplex
Half-Duplex
  Ex. Walkie-Talkie
Full-Duplex
  Ex. Telephone

## Slide 4: Synchronous/Asynchronous
來源: http://wiki.csie.ncku.edu.tw/embedded/USART
Synchronous
  A clock signal is required
  Need to take clock skew into consideration
  Consume more power -> clock gating
  (extra circuit, extra delay from synchronous)
  Less information within a single transmission
Asynchronous
  Add extra information when transmit data
  Low cost and setup time
  Can communicate between machines with different clock
  Less information within a single transmission
Notes: http://wiki.csie.ncku.edu.tw/embedded/USART#synchronous-%E5%90%8C%E6%AD%A5%E5%82%B3%E8%BC%B8

## Slide 5: ModBus over EIA-485
A serial communications protocol
Originally published by Modicon (now Schneider Electric) in 1979
For use with its programmable logic controllers (PLCs)
Has become a standard communication protocol and a commonly available means of connecting industrial electronic devices
  openly published and royalty-free
  relatively easy to deploy and maintain
  places few restrictions
Notes: https://zh.wikipedia.org/wiki/Modbus
1970’s

## Slide 6: Controller Area Network (CAN or CAN bus) over EIA-485
CAN Bus is an automotive bus developed by Robert Bosch
quickly gained acceptance into the automotive and aerospace industries
資料來源: https://canbuskit.fortin.ca/what.php
connect individual systems and sensors as an alternative to conventional multi-wire looms.
allows automotive components to communicate on a single or dual-wire networked data bus up to 1Mbps
Notes: https://canbuskit.fortin.ca/what.php
1980’s

## Slide 7: UART v.s. USART

## Slide 8: Comparison to EIA-232 & EIA-485
 | EIA-232 | EIA-485
Voltage System | Voltage level-based | Differential
Total Drivers and Receivers | 1 Driver, 1 Receiver | 32 Drivers, 32 Receivers
Line Configuration | Point-to-point | Multidrop
Maximum Operational Distance | 15M / 50FT | 1,200M / 3000FT
Maximum Transmission Rate | 1MBit/s | 10MBit/s
Duplex Mode | Full Duplex | Half Duplex or Full Duplex
Receiver Input Voltage Range | +/-15V | -7V to +12V
資料來源: https://www.seeedstudio.com/blog/2019/12/06/what-is-rs485-and-its-difference-between-rs232/
Notes: https://www.researchgate.net/figure/2-Traditional-electrical-architecture-based-on-the-CAN-bus-technology-is-shown-at-the_fig1_288994853
https://www.csselectronics.com/screen/page/simple-intro-to-can-bus/language/en
https://kknews.cc/zh-tw/tech/2qm58qe.html
https://www.optcore.net/difference-between-rs-232-rs-422-and-rs-485/

## Slide 9: Voltage level-based v.s. Differential
Voltage level-based
Differential
資料來源: https://blog.csdn.net/whuzm08/article/details/80431099

## Slide 10
資料來源: https://www.programmersought.com/article/17333563648/
Notes: https://www.alicat.com/rs-232-communication-protocol-alicat-instrument/

## Slide 11: Hardware components
SG90 Servo
MAX485 UART to EIA-485 converter
10kΩ VR
Arduino NANO

## Slide 12: MAX-485 UART-to-RS485 Converter Pin out
Vcc: Circuit Voltage Input
GND: Ground
A:
B:
DI: Data In
RO: Receive Out
DE: Data Enable
RE: Receive Enable
} Data Logic Pin
Notes: 邏輯狀態1（off）和0（on），若A電壓比B要低（A-, B+），其狀態為1，若反過來（A+, B-），其狀態為0，不過標準中沒有定義這兩個狀態的邏輯功能。

## Slide 13: Pinout diagram for Arduino Nano

## Slide 14: Wiring Diagram

## Slide 15: Example

## Slide 16: Homework :
Use potential meter to control servo via EIA-485 bus
Control
React

## Slide 17: Arduino Examples
Regarding how to use servo,
you can refer to the arduino example